## Slide 1: UWW Tier 1 Training Ellen Bailey ellen.bailey@usu.edu 801-536-4432

## Slide 2: Utah Water Watch
Partnership between USU Extension and the DWQ
Started in 2012
Trained 750+ volunteers, monitoring 250+ sites

## Slide 3
Goals:
  Increase the public’s knowledge about water quality
  Collect credible data for water managers to use
Create a network of trained volunteers
Engage and empower our volunteers
Encourage protection through education
Utah Water Watch

## Slide 4: Why do we monitor?
Want to have more information
  Identify current conditions
  Show changes and trends
  Identify problems or solutions
Why monitor water quality?
  We all use water
  Increase our knowledge about the environment
  It’s the LAW!

## Slide 5: Do you have experience monitoring?

## Slide 6: What is citizen science?
Provides an opportunity for citizens to engage in the scientific process to address problems

## Slide 7: Who monitors?
Local: Municipal (City, County) and Private
State: Watershed Coordinators & DWQ
Federal: BLM, USFS, NRCS, etc.
Volunteers!

## Slide 8: Why do we need volunteers?
How many lakes are there in Utah?
  2,085
How many miles of streams?
  14,750 miles of permanent streams
  +89,000 miles of intermittent streams

## Slide 9: What is a watershed?
Geographic area within which all water drains to a common point.

## Slide 10: Watersheds are defined by structure and by function
Structure: How is it formed
Lakes / Rivers / Wetlands
Mountains / Valleys
Geology
Precipitation
Land use
Function: What does it do?
Processes water – but what else?
Notes: Structure: How is it formed?
Function: What does it do?

## Slide 11: Connection between watersheds and water quality?
Everything that happens in a watershed can affect the quality of the water downstream
….“we all live downstream”

## Slide 12: The scale you work at depends on the question you want to answer.
Nested watersheds

## Slide 14: What is Clean Water?
Safe to drink ?
Distilled?
Crystal clear?

## Slide 15: There is no single definition of clean water.
The Clean Water Act defines clean water according to how we use it.
Drinking water
Agriculture
Recreation
Fisheries and aquatic life
Aesthetics
Great Salt Lake

## Slide 16: Water quality is regulated through the Clean Water Act (1972)
Waters of U.S. must be “fishable and swimmable” by 1983
Eliminate all pollution discharge to waters by 1985
Cuyahoga River, June 22 1969
http://blog.cleveland.com/metro/2009/06/cuyahoga_river_fire_40_years_a.html

## Slide 17: Water Quality Standards
Clean Water Act (CWA) regulates the amount of pollutants that enter US Waters from point sources
Types of pollution
  Point Source
  Nonpoint Source

## Slide 18: Pollution source types:
Point sources
Nonpoint sources

## Slide 19: Utah Water Watch monitors:
Physical:
  Temperature
  Turbidity
  Habitat
Chemical:
  pH
  Dissolved oxygen
Biological:
  E. coli (bacteria)
  Macroinvertebrates
Qualitative:
  Weather
  Photos
  Other observations

## Slide 20: Why do we care about temperature?
Fish and other aquatic life
Other effects from temperature…
  How much oxygen water can absorb
  The toxicity of ammonia
Fish and other aquatic life require:
Cold water fish: 20°C
Warm water fish: 27°C

## Slide 21: What causes temperature to rise?
Natural causes:
  Seasons
  Length of river
  Location of river
  Hot springs
Human causes:
  Removal of streamside vegetation (shade)
  Runoff over concrete and other heated surfaces
  Changes in stream shape
  Reductions in flow
  Impoundments
  Industrial discharges

## Slide 22: Why do we care about dissolved oxygen?
Fish and other aquatic life
Other effects from dissolved oxygen…
  Oxygen in water affects solubility of metals and other chemicals
Fish and other aquatic life require:
Cold water fish: 6.5 mg/L
Warm water fish: 5.5 mg/L

## Slide 23: What causes oxygen concentrations to change?
Natural causes
  Uptake by organisms
  Natural increases in temperature
  Quiet water (low re-oxygenation) vs. turbulent waters
Human causes
  Any source of biological material that will decay in water
  High temperatures or low flows
  Excessive plant growth in water

## Slide 24: pH
pH Scale:
0.0 |  |  |  |  |  |  | 7.0 |  |  |  |  |  |  | 14.0 | 
Pure Hydrochloric Acid
Lemon Juice
Rain
Water
5.6
Vinegar, Wine, Orange Juice
Milk
Bleach
Sea Water
Household Ammonia
Oven Cleaner
Gastric Fluids
Baking Soda
Pure Sodium Hydroxide

## Slide 25: Why do we care about pH?
Low pH can affect membranes (e.g. gills of fish or macroinvertebrates and eggs)
At low pH, causes some metals to dissolve into a more toxic form
At high pH, ammonia is more toxic
An acceptable pH range is 6.5-9.0

## Slide 26: What causes pH to rise or fall?
Natural causes:
  Rain is naturally acidic
  Rapid snow melt
  Photosynthesis in water  higher pH
Human causes:
  Combustion causes acids in the atmosphere  acid precipitation
  Industrial discharge
  Mine drainage

## Slide 27: Why do we care about turbidity? Turbidity refers to sediments in streams and lakes
Fills space between cobble in stream and smother fish eggs and tiny aquatic life
Very cloudy water affects visual predators
Sediments fill in reservoirs
Sediments bring nutrients, metals, and more into water

## Slide 28: What are sources of sediment in rivers?
Natural causes:
  Natural “reworking” of flood plain as stream meanders
  Remobilized bedload sediment under high flows
  Seasonal effects
Human causes:
  Runoff (construction, agriculture, forestry, mining)
  Stream bank erosion
Turbidity should not increase rapidly from site to site:
An increase of more than 10 NTUs violates water quality criteria

## Slide 29: Why do we care about E. Coli (bacteria)
E. coli can make people sick
  Concern in drinking water
  Recteation
    Swimming (contact recreation)
    Boating (non-contact recreation)
Contact recreation: 409 colonies/100ml
Drinking water and non-contact recreation: 668 colonies/100ml

## Slide 30: What are the sources of E. coli?
Natural causes:
  Lives in the intestines of warm blooded animals
  Birds and other mammals
Human causes:
  Not picking up after dogs
  Failing septic systems or wastewater treatment plants
  Animal feeding operations (manure)

## Slide 31: Photo point monitoring
Simple way to monitor change.
Riparian area, erosion, seasons, etc.
  Things to consider when determining a site:
  What are the changes we are looking to document?
  Will the photo capture the “area of interest”?
  Is this location consistently easy to access?
  Will the location of the photo point need to change over time? (ideally no)

## Slide 32: Photopoint monitoring
Simple way to monitor change
Taking the picture at the same location and angle each time
Basic instructions for streams: photo taken upstream and downstream from the monitoring site.
Basic instructions for lakes: take a photo in both directions along the lake shore capturing both the bank and water
Photos are uploaded into a shared Google Drive – we will share a link

## Slide 33: Harmful Algal Blooms
What are harmful algal blooms?
Harmful algal blooms (HABs) are large growths of cyanobacteria that change the water color or form surface scums, and occur in lakes, reservoirs and ponds.
Cyanobacteria blooms are occurring more frequently in Utah, likely in response to increased nutrients and a warmer climate.
These tiny plant-like bacteria can produce deadly toxins that are harmful to humans, livestock and pets.
If you are concerned there may be HABs present
  Use caution – avoid ingesting the water or inhaling boat spray, wash hands thoroughly after coming into contact
  Contact us
  Take photos
  Collect a sample if possible, wearing gloves, and drop off to a nearby microscope location (Weber Health Department in Ogden, Salt Lake County USU Extension)

## Slide 34: Macroinvertebrates
Indicators of water quality
Good indicators, pollution sensitive :
Poor indicators, pollution tolerant :

## Slide 35: Water is not static
It has regular seasonal and daily fluctuations.

## Slide 36: Daily manually measuring DO
Chart: Typical Dissolved Oxygen in East Canyon Creek
| 40363.5 | 40364.5 | 40365.510416666664 | 40366.572916666664 | 40367.5 | 40368.5 | 40369.520833333336
 | 10.4 | 10.4 | 10.2 | 9.9 | 9.8 | 10 | 10

## Slide 37: Continuous measuring dissolved oxygen
Chart: Typical Dissolved Oxygen in East Canyon Creek
Point | 10.4 | 10.4 | 10.2 | 9.9 | 9.8 | 10 | 10

## Slide 38: Understand your site
Each site will have unique characteristics
    Some streams are naturally clear while others are naturally turbid
Monitor the site long term to capture the changes
Documenting field parameters on the data sheets help understand the site and current conditions
  Flow, algae, water color, water odor, etc.

## Slide 39: Database
https://uww.usu.edu
For photos, we will share a link where you can upload your photos to a Google Drive

## Slide 40: Quality Control
Follow procedures in your field notebook
  Also available online with videos
Ensure use of the proper units (ᵒC vs ᵒF) and decimals are correct
Enter data into the database (https://uww.usu.edu)
Keep all copies of your field sheet and scan to the Utah Water Watch program coordinator at the end of the year
Make sure equipment is stored properly and follow decontamination procedures

## Slide 41: Safety!
Safety is always more important than the data!
  Be aware of slippery banks or ice
  Don’t let students enter water over their knees or that is moving very fast (more than 1 foot per second)
  Watch for poison ivy, broken glass or other hazards
  Review the Sampling Safety guide

## Slide 42: Resources
http://extension.usu.edu/utahwaterwatch
Instructions
Events
Maps
Photos
Also,
http://extension.usu.edu/waterquality
http://streamsidescience.usu.edu
www.utahcleanwater.org

## Slide 43: For more information:
Ellen Bailey
Utah Water Watch Program Coordinator
Ellen.bailey@usu.edu
801-536-4432
USU Water Quality Extension
435-797-2580, waterquality@usu.edu
http://extension.usu.edu/waterquality